## Slide 1
Environmental aspects of lighting
ISSUES FROM A LIFE CYCLE PERSPECTIVE
Jessika Luth Richter, PhD researcher
IIIEE, Lund University

## Slide 2: Environmental Impacts from Lighting Products
Overview of the environmental impacts from lighting products
Update on current revision of EU green public procurement for street lighting

## Slide 3
Inputs
Outputs
Product’s lifecycle
Manufacturing
Distribution
Use
End-of-Life Management
Raw materials
Life cycle system

## Slide 4: Inventory and system boundaries
Outputs to Ecosphere:
Emissions to air, water and soil, hazardous waste, e-waste
Manufacturing I LED chips packages
Raw Materials
Transport to POS/EU
Use Phase (electricity use)
End-of-Life treatment
Transport
to manufacturer I
Collection & transport to EoL
Inputs from Ecosphere:
Land, resources (energy carriers, metals, rare earths, crude oil, water, process chemicals)
Manufacturing II LED lamps, luminaires
Transport
to manufacturer II

## Slide 5: LED production
SSL value chain
Source: Driel & Fan (2013
  This stage can have higher scores when considering single indicators (e.g. metal depletion or human toxicity)
The production of an LED electronic driver also has a significant impact
  many processes in manufacturing a printed circuit board
Largest environmental impact in this stage are the aluminium parts (e.g., heat sink), electronics (the driver) and LED packaging.
  Heat sinks have been decreasing in size and using different materials recently

## Slide 6
Source: Defra, 2009

## Slide 7
Source: Scholand & Dillon, US Department of Energy, 2012
Comparison of manufacturing, transport and use stages

## Slide 8
Total life-cycle impacts of 4 street lighting technologies in 3 impact categories. 100 % represents the impacts of the HPS luminaire
Source: Dale et al. (2011).

## Slide 9: Largest Impact Areas
The largest environmental impact is linked to the use phase (usually >80%)
The second largest impact is in the manufacturing stage (varies 2-20%)
The impacts of the transport phase only account for 1% - 2% of total.
End-of-life management for SSL is generally low
  Can be a little higher for fluorescent (max 15%)
Source: Solid State Lighting Annex – Life Cycle Assessment of Solid State Lighting Final Report (2014) Energy Efficient End-Use Equipment (4E), International Energy Agency

## Slide 10: Life cycle environmental aspects
The two most significant parameters contributing to the environmental impacts of lighting products are luminous efficacy (lm/W) and useful life (hours of operation during lifetime).
Electricity mix and product development matters
  Improving efficiencies are more important than long lifetimes (from LCA perspective) in electricity mixes with fossil fuel (e.g. EU average)
  In decarbonised energy mixes (e.g. in Swedish mix) useful life is more important than in
Source: Solid State Lighting Annex – Life Cycle Assessment of Solid State Lighting Final Report (2014) Energy Efficient End-Use Equipment (4E), International Energy Agency

## Slide 11
Chart: Relative impact %
| Climate change | Ozone depletion | Terrestrial acidification | Freshwater eutrophication | Marine eutrophication | Human toxicity | Photochemical oxidant formation | Particulate matter formation | Terrestrial ecotoxicity | Freshwater ecotoxicity | Marine ecotoxicity | Ionising radiation | Agricultural land occupation | Urban land occupation | Natural land transformation | Water depletion | Metal depletion | Fossil depletion
12500h, energy efficient replacement | 83.5398 | 82.4825 | 88.845 | 98.0225 | 100 | 100 | 92.0919 | 93.5497 | 100 | 100 | 100 | 76.8579 | 80.08 | 100 | 89.8229 | 79.8684 | 100 | 83.0395
25000h | 100 | 100 | 100 | 100 | 92.8779 | 80.3538 | 100 | 100 | 79.6815 | 93.4403 | 90.6853 | 100 | 100 | 94.9839 | 100 | 100 | 60.3411 | 100
EU average electricity mix

## Slide 12
Swedish electricity mix
Chart: %
| Climate change | Ozone depletion | Terrestrial acidification | Freshwater eutrophication | Marine eutrophication | Human toxicity | Photochemical oxidant formation | Particulate matter formation | Terrestrial ecotoxicity | Freshwater ecotoxicity | Marine ecotoxicity | Ionising radiation | Agricultural land occupation | Urban land occupation | Natural land transformation | Water depletion | Metal depletion | Fossil depletion
12500, energy and material efficient replacement | 100 | 84.6224 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 81.9344 | 82.3855 | 100 | 94.8131 | 83.8979 | 100 | 100
25000 | 92.0599 | 100 | 90.7472 | 76.0087 | 87.0094 | 75.8614 | 93.6875 | 89.8365 | 85.8709 | 89.1112 | 80.1592 | 100 | 100 | 98.7737 | 100 | 100 | 82.408 | 91.251

## Slide 13: Other environmental issues in life cycle
Lighting Pollution
Lighting Pollution
Rapid changes in design
  How to influence ecodesign
    Standardization (Zhaga)?
    Modularity / upgradeability

## Slide 14: Impact categories (e.g.)
Resource use
energy and materials
water
land (including wetlands)
landfill
Human health
toxic impacts
non-toxic impacts
impacts in work environment
Ecological impacts
Global warming
Ozone depletion
Acidification
Eutrophication
Photochemical oxidation
Eco-toxic impacts
Biodiversity
Light pollution?
…

## Slide 15: Other environmental issues in life cycle
Light Pollution
  Ecological but also health impacts of lighting
Rapid changes in design
  How to influence ecodesign
    Extended lifetimes (Standards? Warranties)
    Modularity / upgradeability /repairability
    Availability of spare parts
    Standardization (Zhaga)?
    Use of recycled materials?
Notes: These are being discussed as part of EU Ecodesign regulations for lighting, but lots of questions still and progress is slow. Main focus continues to be on energy efficiency and quality requirements. More happening with GPP currently.

## Slide 16
Notes: LCA and LCC approaches underpin GPP

## Slide 17: Two levels of criteria
Core
  Focus on key areas
Comprehensive
  More aspects considered
  Higher level of ambition
Core
Comprehensive

## Slide 18: Life cycle perspective incorporated in GPP
Lowest life cycle cost awarded points
  Time period
  Real interest /discount rate (%)
  Electricity price (kr/kWh)
  Annual electricity price change (apart from inflation) (%)
  Investment costs (kr)
  Running & maintenance costs
  Reduction factor for automation:
    e.g. Daylight detection (0.8) x Motion-detection (0.75) = 0.6
    https://www.upphandlingsmyndigheten.se/en/subject-areas/lcc-tools/

## Slide 19: Revised and new GPP criteria
Lifetime extension
Proposed warranties of min. 4 years
  Industry divided
  case by case?
  Some asking for 8 years
Ensure reparability
  Diagram to aid repair
  Guarantee of accessibility (i.e. able to use common tools)
  Availability of spare parts
    Enforcement?
Source: Seattle Municipal Archives.

## Slide 20: Light Pollution
  Max light above horizon is not more than 1%
  Sensitive areas
    CCT≤ 3000k, CRI < 70
Source: U.S. National Park Service

## Slide 21: Others
  Points for metering and measuring
    Plays a strategic role in overcoming challenges,
      improve maintenance processes
      reducing energy consumption
      communicating CO2 savings
Source: U.S. Air Force

## Slide 22: GPP revision process
150 members observing process
Workshop in Seville in November 2016
  Preliminary report on technical and environmental performance
Comments on draft document in February 2017, final document October 2017
Mostly industry and NGOs

## Slide 23: Other environmental issues in life cycle
Critical materials and embodied impacts
Rebound

## Slide 24
Source: Gielen, 2011

## Slide 25: White Light
YEu Oxide
Eu oxide
La Oxide
Tb Oxide
Ce Oxide
Others
Others
Blue LED (e.g. InGaN)
Yellow phosphor (e.g. YAG/CASN – containing Y, EU, Ce)*
*YAG = (Y0.98Ce0.02)3Al5O12; CASN = Ca0.98Eu0.02AlSiN3)

## Slide 26
Source: EU Commission, 2014

## Slide 27: Example: impacts of mining rare earths
Images: Unknown Fields Project
Complex global value chains for materials make it difficult to avoid
Starting to see material certification for conflict materials (e.g. conflict-free tin, tantalum, gold, etc.)
Notes: Environmental impacts:
land use
leachate into groundwater (e.g. heavy metals, arsenic, fluorides, sulphides, thorium and uranium)
dusts emissions ( with contents of e.g. heavy metals, thorium, uranium)
Air emission of process chemicals (SO2, HCl)
waste water generation
GHG emissions due to energy use

## Slide 28: Recycling Critical elements
Source: UNEP, 2011
Notes: Recycling almost non-existent for most critical materials in lighting. It will prove technically difficult to recover from LEDs due to small amounts and low prices of primary material production. Another strategy is to ensure lifetimes.

## Slide 29: Dealing with rebound
  Framing and formulation of efficiency goals
    Focus on function as well as efficiency
    Decide what will be done with energy and monetary savings to avoid unwanted rebound
    Maximum lighting requirements as well as minimum?
Right light at the right place at the right time
    Focus on what contributes to wellbeing

## Slide 30: Environmental aspects for lighting - summary
Extending life cycle thinking beyond energy efficiency
  Extending lifetimes through warranties, standardization, modularity, repairability, availability of spare parts
Addressing issues still constrained by what is possible to measure and enforce
Additional resources:
I4E Solid State Lighting: https://ssl.iea-4e.org/
EU: http://susproc.jrc.ec.europa.eu/Street_lighting_and_Traffic_signs/index.html
ICLEI: http://www.iclei.org/activities/agendas/sustainable-local-economy-and-procurement.html